## Slide 1
CHAPTER 4
FUNCTIONAL ORGANIZATION
Computer Architecture &
Networks

## Slide 2: LEARNING OUTCOMES
To learn and understand ;
Instruction Pipelining
Introduction to Instruction-Level Parallelism (ILP)

## Slide 3: Today………
3
Instruction Pipelining and Instruction-level Parallelism
Pipeline Strategy
Pipeline Performance
Pipeline hazards
Dealing with branches
Superscalar Systems
Instruction-level Parallelism

## Slide 4: Pipelining Strategy
Similar to the use of an assembly line in a manufacturing plant
New inputs are accepted at one end before previously accepted inputs appear as outputs at the other end
4
To apply this concept to instruction execution we must recognize that an instruction has a number of stages
类似于在制造厂中使用装配线
在先前接受的输入显示为另一端的输出之前，在一端接受新输入
要将此概念应用于指令执行，我们必须认识到指令有多个阶段

## Slide 5: Pipelining
Pipelining overlaps the execution of multiple instructions in parallel 流水线重叠并行执行多条指令
Data path is divided into stages which all operate simultaneously 数据路径分为多个阶段，所有阶段同时运行
Pipeline stages ideally have to have the same time (clock cycle) 理想情况下，管道级必须具有相同的时间（时钟周期）
Pipeline buffers (latches) prevent data entering next stage before previous data has left
管道缓冲区（锁存器）防止数据在前一个数据离开前进入下一个阶段
Increasing the number of stages allows higher number of overlapped instructions but also increases the total pipeline latch latency 增加阶段数允许更多的重叠指令，但也会增加总的管道锁存延迟

## Slide 6: Two-Stage Instruction Pipeline
6

## Slide 7: Additional Stages
7
Fetch instruction (FI)
Read the next expected instruction into a buffer 将下一条预期指令读入缓冲区
Decode instruction (DI)
Determine the opcode and the operand
specifiers 确定操作码和操作数说明符
Calculate operands (CO)
Calculate the effective address of each
source operand 计算每个源操作数的有效地址
This may involve displacement, register indirect, indirect, or other forms of address calculation 这可能涉及移位、寄存器间接、间接或其他形式的地址计算
Fetch operands (FO)
Fetch each operand from memory 从内存中提取每个操作数
Operands in registers need not be fetched
不需要提取寄存器中的操作数
Execute instruction (EI)
Perform the indicated operation and store the result, if any, in the specified destination operand location
执行指示的操作并将结果（如果有）存储在指定的目标操作数位置
Write operand (WO)
Store the result in memory 将结果存储在内存中
Stage Step
FI > DI > CO > FO > EI > WO
1 + 2 = 3, operand可以是1和2

## Slide 8: Six-stage instruction pipeline
8

## Slide 9: Timing Diagram for Instruction Pipeline Operation
9
[W. Stallings (2013)]
Cycle

## Slide 12: Speedup Factors with Instruction Pipelining
12
[W. Stallings (2013)]

## Slide 13: Pipeline Hazards
Occur when the pipeline, or some portion of the pipeline, must stall because conditions do not permit continued execution
Also referred to as a
pipeline bubble
也称为管道气泡
There are three types of
hazards:
Resource
Data
Control
由于条件不允许继续执行，管道或部分管道必须停止时发生
有三种类型的危害：资源、数据、控制

## Slide 14: Resource Hazards
A resource hazard occurs when two or more instructions that are already in the pipeline need the same resource
The result is that the instructions must be executed in serial rather than parallel for a portion of the pipeline
A resource hazard is sometimes referred to as a structural hazard
Have to wait one clock cycle before it can start
当已经在管道中的两个或多个指令需要相同的资源时，就会发生资源危险
结果是，对于管道的一部分，指令必须串行执行，而不是并行执行
资源危害有时被称为结构危害

## Slide 15: Data Hazards 数据危害
A data hazard occurs when there is a conflict in the access of an operand location
当操作数位置的访问发生冲突时，会发生数据危险

## Slide 16: Types of Data Hazard
Read after write (RAW), or true dependency
An instruction modifies a register or memory location
Succeeding instruction reads data in memory or register location
Hazard occurs if the read takes place before write operation is complete
Write after read (WAR), or antidependency
An instruction reads a register or memory location
Succeeding instruction writes to the location
Hazard occurs if the write operation completes before the read operation takes place
Write after write (WAW), or output dependency
Two instructions both write to the same location
Hazard occurs if the write operations take place in the reverse order of the intended sequence

## Slide 17: Control Hazard 控制危险 Also known as a branch hazard
Occurs when the pipeline makes the wrong decision on a branch prediction 当管道对分支预测做出错误决策时发生
Brings instructions into the pipeline that must subsequently be discarded Dealing with Branches:
Multiple streams
Prefetch branch target
Loop buffer
Branch prediction
Delayed branch
将随后必须丢弃的指令放入管道中处理分支：
多流
预取分支目标
循环缓冲区
分支预测
延迟分支

## Slide 18: Multiple Streams 多流
A simple pipeline suffers a penalty for a branch instruction because it must choose one of two instructions to fetch next and may make the wrong choice
A brute-force approach is to replicate the initial portions of the pipeline and allow the pipeline to fetch both instructions, making use of two streams
Drawbacks:
With multiple pipelines there are contention delays for access to
the registers and to memory
Additional branch instructions may enter the pipeline before the
original branch decision is resolved
简单管道会因分支指令而受到惩罚，因为它必须从两条指令中选择一条来获取下一条指令，并且可能会做出错误的选择
蛮力方法是复制管道的初始部分，并允许管道使用两个流获取两条指令
缺点：
对于多个管道，存在访问的争用延迟将寄存器和内存连接起来
其他分支指令可能会在原始分支决策已解决

## Slide 19
Prefetch Branch Target
预取分支目标
When a conditional branch is recognized, the target of the branch is prefetched, in addition to the instruction following the branch
Target is then saved until the branch
instruction is executed
If the branch is taken, the target has already
been prefetched
IBM 360/91 uses this approach
如果执行了分支，则目标已执行已预取
IBM360/91使用这种方法
然后将目标保存到分支指令被执行
识别条件分支时，除了分支后面的指令外，还将预取分支的目标

## Slide 20: Loop Buffer
Small, very-high speed memory maintained by the instruction fetch stage of the pipeline and
containing the n most recently fetched instructions, in sequence
Benefits:
Instructions fetched in sequence will be available without the usual memory access time
If a branch occurs to a target just a few locations ahead of the address of the branch instruction, the target will already be in the buffer
This strategy is particularly well suited to dealing with loops
Similar in principle to a cache dedicated to instructions
  Differences:
    The loop buffer only retains instructions in sequence
    Is much smaller in size and hence lower in cost

## Slide 22: Branch Prediction
Various techniques can be used to predict whether a branch will be taken:
Predict never taken
Predict always taken
Predict by opcode
Taken/not taken switch
Branch history table
These approaches are static
They do not depend on the execution history up to the time of the conditional branch instruction
These approaches are dynamic
They depend on the execution history

## Slide 23: Constraints
Instruction level parallelism
Refers to the degree to which the instructions of a program can be executed in parallel
A combination of compiler based optimization and hardware techniques can be used to
maximize instruction level parallelism
Limitations:
True data dependency
Procedural dependency
Resource conflicts
Output dependency
Antidependency
ILP = IPC

## Slide 24: Super pipeline

## Slide 25: Superscalar pipeline
Superscalar pipeline introduces the ability to execute instructions independently and concurrently in different pipelines which enables more instructions executed in every clock period. A superscalar processor contains multiple copies of the datapath hardware to execute multiple instructions simultaneously.

## Slide 26: Superscalar

## Slide 28: Design Issues
Instruction-Level Parallelism and Machine Parallelism
Instruction level parallelism
Instructions in a sequence are independent
Execution can be overlapped
Governed by data and procedural dependency
Machine Parallelism
Ability to take advantage of instruction level parallelism
Governed by number of parallel pipelines

## Slide 29: Exercise
Explain what is pipelining
Pipelining is a technique where multiple instructions are overlapped during execution. Pipeline is divided into stages and these stages are connected with one another to form a pipe like structure. Instructions enter from one end and exit from another end.
2. What are the instructions involve in two-stage instruction pipeline?
The execution time will generally be longer than the fetch time. Execution will involve reading and storing operands and the performance of some operation. Thus, the fetch stage may have to wait for some time before it can empty its buffer.
3. What happen when there are more stages in pipeline?
Increase in the number of pipeline stages increases the number of instructions executed simultaneously.

## Slide 30: Exercise
4. Define and explain every stage in six-stage instruction pipeline
Fetch instruction (FI) - Read the next expected instruction into a buffer
Decode instruction (DI) - Determine the opcode and the operand specifiers
Calculate operands (CO) - Calculate the effective address of each source operand may
involve displacement, register indirect, indirect, or other forms of
address calculation
Fetch operands (FO) - Fetch each operand from memory and Operands in registers need not
be fetched.
Execute instruction (EI) - Perform the indicated operation and store the result, if any, in the
specified destination operand location.
Write operand (WO) - Store the result in memory.
5. What is the effect of conditional branch?
A branch interrupts the normal sequence of program execution.

## Slide 31: Exercise
6. Explain how conditional branch take place
There are two possible next instructions, and in general you don't know which one you want until some computation has taken place, either in the branch instruction itself, or some earlier instruction. (slide10)
7. Explain each of the following hazard;
Resource hazards
A resource hazard occurs when two or more instructions that are already in the pipeline need the same resource. As a result, for part of the pipeline, instructions must be executed serially, not in parallel. A resource hazard is sometimes referred to as a structural hazard.
Data hazards
Data danger occurs when access to operand locations conflicts.
Control hazards
It is also known as a branch hazard. It occurs when the pipeline makes the wrong decision on a branch prediction. It brings instructions into the pipeline that must subsequently be discarded dealing with Branches such as multiple streams, prefetch branch target, loop buffer, branch prediction, and delayed branch.

## Slide 32: Exercise
8. List the limitation of Instruction Level Parallelism (ILP)
- Instructions in a sequence are independent
- Execution can be overlapped
- Governed by data and procedural dependency